## Slide 1: Life Cycle Assessment of Scooters in Berlin
Comparison between Electric, Two-Stroke, and Four-Stroke Models
Presented By:
Mohammed Alyami -

## Slide 2: TABLE OF CONTENTS
Goal & Scope
Functional Unit
01 02
LCIA Method
03
Assumptions and Limitations
04

## Slide 3: TABLE OF CONTENTS
Life Cycle Inventory
05
Conclusions and Recommendations
06

## Slide 4
01
Goal and Scope

## Slide 5: Goal
Compare the environmental impacts of 3 scooters (Electric, Two-Stroke, Four-Stroke) from cradle to
grave in Berlin, Germany
Identify hotspots to propose improvement strategies
Apply Life Cycle Assessment (LCA) approach using openLCA software and ecoinvent 3.6 database

## Slide 6: Scope
Includes all life cycle stages:
Production
Transportation
Use phase
End of Life (manual dismantling and disposal)
Focus area: Berlin, Germany

## Slide 7
02
Functional Unit

## Slide 8: Functional Unit
Functional Unit: 1 person-kilometer (p*km)
Total distance considered: 55,000 p*km (50,000 km * 1.1 passengers)

## Slide 9
03
LCIA
Method

## Slide 10: LCIA Method
Method: ReCiPe 2016 Midpoint (H)
Covers Global Warming, Fossil Resource Scarcity, Human Toxicity, Particulate Matter, etc.
Same method applied to all scooters for fair comparison

## Slide 11
04
Assumptions and Limitations

## Slide 12: Assumptions
Life expectancy same for all scooters: 50,000 km
Battery and charger for electric scooter assumed to be produced in China
One battery assumed for entire life of electric scooter
Manual dismantling assumed for all models
Use phase modeled for emissions, road maintenance, etc. based on literature and ecoinvent database

## Slide 13: Limitations
Two-stroke and Four-stroke scooters modeled as same production process (although
real-life processes may differ)
Emissions data for Four-stroke partly based on modified Two-stroke values
Only selected emissions compounds considered
Electric scooter battery data not specific for scooters (general EV battery models used)

## Slide 14
05
Life Cycle Inventory

## Slide 15: Life Cycle Inventory: Production
Electric scooter production excludes battery.
Two-stroke and Four-stroke scooters modeled the same for production (only weight differs).
Two battery production scenarios modeled for electric scooter:
  (1) Generic ecoinvent battery.
  (2) Frankfurt Airport battery.
Production process selection depends on scooter model and battery scenario.

## Slide 16: Life Cycle Inventory: Transportation
Two-stroke and Four-stroke scooters transported from Asia:
  Ship → Rotterdam
  Train → Berlin
  Lorry → City center
Electric scooter transported from Italy:
  Lorry → Milan
  Train → Berlin
  Lorry → City center
Transportation routes and distances affect emissions and impacts.

## Slide 17: Life Cycle Inventory: Use Phase
Electric scooter:
  Requires electricity → 4.128 kWh per charge, 500 charges total.
  Three electricity mixes considered:
    ecoinvent average
    German Green Mix
    Airport electricity mix
  Electricity source strongly affects impacts (especially global warming).
Fuel scooters:
  Two-stroke fuel consumption → 40.8 km/L
  Four-stroke fuel consumption → 45.45 km/L
  Emissions calculated from real emission factors → adjusted using literature.
Use phase is dominant for two-stroke emissions.
Road use, road maintenance, and scooter maintenance impacts also included during use phase.

## Slide 18: Life Cycle Inventory: End of Life
Manual dismantling assumed for all scooters.
Process modeled based on electric scooter and passenger car dismantling data.
Materials sorted for recycling, reuse, and disposal.
End of life process impacts included in LCA.

## Slide 19: Life Cycle Impact Assessment (LCIA) Results Summary
Use phase dominates Two-stroke impacts (CO, VOCs, particulates)
Four-stroke better but higher NOx
Electric scooter shows lowest use-phase emissions, but sensitive to electricity mix and battery type

## Slide 20
06
Conclusions and Recommendations

## Slide 21: Conclusions
No clear best scooter
Two-stroke is the worst for urban air quality
Four-stroke better, but emissions still considerable
Electric best if powered by green energy; worst if electricity is fossil-fueled

## Slide 22: Recommendations
Promote greener electricity to improve electric scooter LCA
Gradual phase-out of Two-stroke scooters
Encourage recyclable and eco-designed scooters
More accurate data collection needed for precise LCA in future

## Slide 23: THANKS!